## Slide 1
Grounded CAD: Natural-Language Editing of STEP Models
Team: Night_Owls
Reiki Tanaya Karuka
Department of Mechanical engineering
rkaruka@mtu.edu
Lenin Goud
Department of Computer Science
Lathikam@mtu.edu
IDETC 2026 - Problem Statement 3

## Slide 2: Motivation:
CAD edits are slow when engineers must manually find features, rebuild geometry, and validate every change.
Grounded CAD edits existing STEP files from natural-language instructions.
Benchmark success depends on changing the intended feature, not just producing a valid CAD file.

## Slide 3: Grounded CAD: Harness Architecture
Parquet File
.Step
Grounder
Classifier
Planner
Executor
Verifier
Critic
Output
No
Yes
Grounder - extracts a compact B-Rep census: faces, rims, holes, bounding boxes, and edit sites.
Classifier - routes the instruction into typed edit slots.
Planner - selects deterministic tools or GPT-written local CadQuery.
Executor - runs edits in an isolated watchdog process.
Verifier/Critic - rejects bad outputs and turns failure buckets into retry feedback.

## Slide 4: Grounded CAD: What changed during development
The final harness moved away from direct STEP text edits and image-only prompting. It uses STEP-derived geometry facts, true orthographic CAD views, isolated CadQuery execution, and per-row scoring.
Key fixes included provenance-safe fresh runs, watchdog handling, identity-output rejection, true axis-aligned view rendering, candidate enumeration for local edits, and detailed failure buckets for targeted debugging.

## Slide 5: Grounded CAD: Results
Current interpretation: Chamfer and Volume F1 stay relatively high when outputs are valid, but Diff F1 drops when the edit lands on the wrong feature. The next improvement target is therefore feature grounding, not whole-part reconstruction.

## Slide 6: Grounded CAD: Cost Efficiency & Scalability
Token efficiency
The harness avoids sending full STEP text to the model.
Instead, it sends compact geometry summaries, orthographic view sheets, parsed dimensions, and targeted retry feedback.
Deterministic candidates handle cheap local edits before spending GPT calls.
Scalability safeguards
Each row runs in a child process with a watchdog.
Large assemblies skip expensive source rendering when it risks freezing the benchmark.
Timeouts are no longer scored as ordinary valid predictions.

## Slide 7: Grounded CAD: Visual evidence and examples
Initial Model | Grounded CAD
Example rows compare the original STEP-derived views with the edited output. The table is intentionally visual: it helps diagnose whether a low D score is caused by no-op output, wrong target selection, or a real but incomplete edit.

## Slide 8: Ablation Study: What actually affected Diff F1
Key finding: structured geometry and failure buckets mattered more than extra images alone.
Agent | Success Rate
Grounder | 
Classifier | 
Planner | 
Executor | 
Verifier | 
Critic | 
Strong target facts
Important routing
Scope control
Must be isolated
Rejects no-op
Useful as feedback

## Slide 9: Limitations, Observations, and Next Steps
Main limitation: The system can create valid geometry but still lose Diff F1 when it chooses the wrong edge, hole, face, or side of the part.
Observation: Direct STEP line edits are not reliable because STEP topology is interlinked. CadQuery/B-Rep operations are safer for producing valid edited solids.
Next step: Use failure buckets as control signals. When a row is tagged wrong_edge_or_scope, force re-grounding to alternate candidate features before accepting the edit.
Future scope: stronger B-Rep target matching, operation-specific validators, and a final fresh 48-row evaluation before claiming benchmark improvement.